## Slide 1: Basic DFT Training
DMD/DTM 2019
KenChi

## Slide 2: Agenda
Why need DFT
What’s DFT
Scan - fault model
Scan - basic
Ac scan - fault model
Ac scan - on-chip clock chop
Ac scan - test clock plan
Mbist - structure
Mbist – Algorithm example
IOLT
Faraday test integration platform
Pattern format
Utility for test Pattern

## Slide 3: Why need DFT
100% yield is NOT possible, fabrication defects will always present.
Classification of physical defects :
  [Manufacture]
  dust particles (fig. a)
  Mask contamination, Fabrication area contamination (fig. b)
  Process Variation (fig. c)
  [Aging Effects]
  Electro migration (metal migration) (fig. d)
  Oxide degradation
  [Handling]
  ESD

## Slide 4: Why need DFT
In View of quality
assume natural yield is 90%
, which means 100000 fail die per million
The number show we must have a high-coverage test for screening out fail dies
In View of test cost
Rule of ten
DFT is the abbreviation of “Design-For-Test”
Chip-level test circuit, as a part of design.
high test coverage and low test cost.
Chip Level
Board Level
System Level
Package Level
Test
Cost
10X
10X
10X

## Slide 5: Why need DFT
Pros.
  Accelerate the testing process
  Guarantee the quality of chips
Cons.
  Overhead in chip area
Basic role of test
  Separating good dies from bad dies
Expanded role of test
  Feedback for yield learning/ramping
  Screening out weak dies (reliability)

## Slide 6: What’s DFT
[Defect-based Test]
Identify physical defect
Convert physical defect to logic fault model and parameter fault model
Decide test method/algorithm to target the certain fault model
PD_MPC220
PD_MCP100
PD_ALIVE
PD_PCIE
PD_LCDC
PD_ISP
PD_USBOTG
PD_SATA
Circuit open/short
cmos stuck on/
short
bridges
geometric distortion
Process variation

## Slide 7: What’s DFT
Convert physical defect to fault model
Logical faults
– the fault change the logic function of the circuit
  Stuck-at : net stuck at a logic 0/1
  Bridging : value on one net affects another net
  Coupling : transition on one net affects another net
Parametric faults
- the fault alter physical properties other than logic function
  Delay / Transition
  Coupling : transition on one net affects another net
  IDDQ
  DC Level

## Slide 8: What’s DFT
A example of the fault models that supported by Mentor Graphic

## Slide 9: Scan – stuck-at fault model
Many different physical defects may be modeled by the same logical stuck-at fault.
Complexity is greatly reduced.

## Slide 10: Scan – concept
Port A
SO
Y
D
Q
D
Q
D
Q
SE
CLK
SI
SA0
1
1
0
0
For example, to detect a stuck-at-0 fault site, which is behind AND gate.
Place logic-1 at AND’s output (prove it’s not stuck-at 0)
In order to place logic-1 at AND’s output , certain logic-value should be placed in
the input side of the logic cone.
The logic-1 can be captured by DFF, and shift-out for observation
1
In order to achieve item1,2,3, all DFFs is needed to be chained up,
which is so-called scan chain

## Slide 11: Scan – basic steps
Port A
SO
Y
D
Q
D
Q
D
Q
SE
CLK
SI
In order to achieve item1,2,3, all DFFs is needed to be chained up,
which is so-called scan chain
LOAD / UNLOAD
FORCE PI
MEASURE PO
PULSE CAPTURE CLK
Load – shift in vale for control
UnLoad – shift out for observation
0
1
X
Detect SA0, Required : 1

## Slide 12: Scan – basic steps
Port A
SO
Y
D
Q
D
Q
D
Q
SE
CLK
SI
Detect SA0, Required : 1
In order to achieve item1,2,3, all DFFs is needed to be chained up,
which is so-called scan chain
LOAD / UNLOAD
FORCE PI
MEASURE PO
PULSE CAPTURE CLK
Load – shift in vale for control
UnLoad – shift out for observation
0
1
X
0
1

## Slide 13: Scan – basic steps
Port A
SO
Y
D
Q
D
Q
D
Q
SE
CLK
SI
In order to achieve item1,2,3, all DFFs is needed to be chained up,
which is so-called scan chain
LOAD / UNLOAD
FORCE PI
MEASURE PO
PULSE CAPTURE CLK
Load – shift in vale for control
UnLoad – shift out for observation
0
1
X
0
1
1
Detect SA0, Required : 1

## Slide 14: Scan – basic steps
Port A
SO
Y
D
Q
D
Q
D
Q
SE
CLK
SI
In order to achieve item1,2,3, all DFFs is needed to be chained up,
which is so-called scan chain
LOAD / UNLOAD
FORCE PI
MEASURE PO
PULSE CAPTURE CLK
Load – shift in vale for control
UnLoad – shift out for observation
X->1
0
1
1
Detect SA0, Required : 1
0->0
1->1

## Slide 15: Scan – basic steps
Port A
SO
Y
D
Q
D
Q
D
Q
SE
CLK
SI
In order to achieve item1,2,3, all DFFs is needed to be chained up,
which is so-called scan chain
LOAD / UNLOAD
FORCE PI
MEASURE PO
PULSE CAPTURE CLK
Load – shift in vale for control
UnLoad – shift out for observation
1
Detect SA0, Required : 1
0
1

## Slide 16: Scan – test compression
Benefit of test compression :
Reduce test cost
Reduce shared-io for scan-in and scan-out

## Slide 17: ac Scan – basic & OCC
Port A
SO
Y
D
Q
D
Q
D
Q
SE
SI
PLL
OCC
cap_en->ON
At-scan share the same circuit with normal scan
Additionally, at-scan required a at-speed double-capture clk pulse.
Occ, onchip-clock-chop help to generate the double-capture-pulse from PLL.

## Slide 18: ac Scan – Transitional delay fault model
The concept is similar to Stuck-at fault model
Two types of fault :
  Slow-to-Rise
  Slow-to-Fall
To detect the fault, DFF’s clock require a double-capture-pulse,
And the transition of a path must be completed within a double-capture-pulse
Slow-to-Rise

## Slide 19: ac Scan – clock plan
The second problem of ac scan is “test clock plan”
The principle of test clock is :
  Test Freq must be identical with functional usage
  If two clock domains are functional timing true path , they should be merged with one occ clock domain.
  If two clock domains are functional timing false path , they shouldn’t be merged into one occ clock domain.

## Slide 20: ac Scan – clock plan
Faraday test Clock Builder (fcb) help to analyze and plan test clock
To meet the principle, the difficulties are :
  Where is the root point of each clock domain ?
  What’s the freq of the domain ?
  What is the interacting condition and timing exception condition between domains ?

## Slide 21: Mem Bist - structure
RAM
Mbist controller
(Algorithm-based pattern generator)
Comparator
TAP Ctrl
Func logic
Func Logic
ADDR
DI
Control
DO
Fail_h
Tap ports

## Slide 22: March C+ Algorithm (1/7)
smeax2
Write 0s (initialize)
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 0s
w0 0
w0 7
w0 6
w0 5
w0 4
w0 3
w0 2
w0 1
Mem Bist – Algorithm Intro
Notes: 先全部寫0

## Slide 23: March C+ Algorithm (2/7)
smeax2
Stuck-At Fault
w1, r1 => sa0
Write 0s (initialize)
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 0s
Transition Fault
w0, r0, w1, r1 => up TF
r0, w1, r1 0
r0, w1, r1 1
r0, w1, r1 2
r0, w1, r1 3
r0, w1, r1 4
r0, w1, r1 5
r0, w1, r1 6
r0, w1, r1 7
Mem Bist – Algorithm Intro

## Slide 24: March C+ Algorithm (3/7)
smeax2
Write 0s (initialize)
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 0s
r1, w0, r0 0
r1, w0, r0 1
r1, w0, r0 2
r1, w0, r0 3
r1, w0, r0 4
r1, w0, r0 5
r1, w0, r0 6
r1, w0, r0 7
Stuck-At Fault
w0, r0 => sa1
Mem Bist – Algorithm Intro

## Slide 25: March C+ Algorithm (4/7)
Write 0s (initialize)
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 1s, Write 0s, Read 0s
Read 0s
Read 0s, Write 1s, Read 1s
smeax2
Coupling Fault
w1, r1 (address n-1)
r1 (address n)
r0, w1, r1 0
r0, w1, r1 1
r0, w1, r1 2
r0, w1, r1 3
r0, w1, r1 4
r0, w1, r1 5
r0, w1, r1 6
r0, w1, r1 7
Mem Bist – Algorithm Intro

## Slide 26: March C+ Algorithm (5/7)
Write 0s (initialize)
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 1s, Write 0s, Read 0s
Read 0s
Read 0s, Write 1s, Read 1s
smeax2
(0-1-1)
(0-1-1-0)
r0, w1, r1 0
r0, w1, r1 1
r0, w1, r1 2
r0, w1, r1 3
r0, w1, r1 4
r0, w1, r1 5
r0, w1, r1 6
r0, w1, r1 7
Mem Bist – Algorithm Intro

## Slide 27: March C+ Algorithm (6/7)
Write 0s (initialize)
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 1s, Write 0s, Read 0s
Read 0s
Read 0s, Write 1s, Read 1s
smeax2
r1, w0, r0 0
r1, w0, r0 1
r1, w0, r0 2
r1, w0, r0 3
r1, w0, r0 4
r1, w0, r0 5
r1, w0, r0 6
r1, w0, r0 7
(0-1-1)
(0-1-1-0)
Mem Bist – Algorithm Intro

## Slide 28: March C+ Algorithm (7/7)
Write 0s (initialize)
Read 0s, Write 1s, Read 1s
Read 1s, Write 0s, Read 0s
Read 1s, Write 0s, Read 0s
Read 0s
Read 0s, Write 1s, Read 1s
smeax2
r0 0
r0 7
r0 6
r0 5
r0 4
r0 3
r0 2
r0 1
Mem Bist – Algorithm Intro

## Slide 29: IOLT
Measure steady-state electrical characteristics
Common Test Items
  Open/Short
  VOL/VOH (IOL/IOH)
  VIL/VIH
  IOZL/IOZH
  IIL/IIH
  RPU/RPD

## Slide 30: IOLT – DC properties
  VIL : max Voltage Input that chip is still sensed as logic Low,
  IIL is the current.
  VIH : min Voltage Input that chip is still sensed as logic High
  IIH is the current.
  VOL/IOL : Verify the ability of an output to provide current (IOL)
  , without exceeding the specified voltage (VOL)
  VOH/IOH : Verify the ability of an output to provide current (IOH)
  , at a specified voltage (VOH)
  RPU/RPD : resistance of pulling circuit
  Leakage : current of IO at Input direction without any pulling

## Slide 31: IOLT – DC properties

## Slide 32: IOLT – circuit
1. To test IOLT, all digital IO will be
chained up by NAND-tree structure.
2. DC characteristics will be tested
one by one.

## Slide 33: Faraday Test Integration Platform
Modern ASIC/SoC design contains variety of test items :
  analog IP
  memory bist blocks
  scan of digital part for Mixed-mode IP
  functional test vectors for Mixed-mode IP
  Top scan
  IOLT
How to plan / integrate these test mode and circuits?
  >> FTIP – faraday test integration platform

## Slide 34: Faraday Test Integration Platform
Phase A
plan test mode decoder
declare test clock / ctrl / obs port

## Slide 35: Faraday Test Integration Platform
Phase B
plan mux-in, mux-out, or internal hookup for each testmode
Output of ftip :
Netlist with the specified test circuit
Partial timing constraints

## Slide 36: Test pattern
Faraday has internal vector format, called FTL.
Advantages is simple for edit.
Four parts to descript test vectors :
- Declare port name and direction
- Descript waveform
- Descript the sequence of vectors
- vectors

## Slide 37: Test pattern utilities
FTL is exchangeable with wgl.
Utilities, Ftl2ver and ftrc, can convert ftl to testbench, and convert fsdb to FTL, respectively
Summary table :
Utility | FUNCTION
ftl2wgl | convert ftl to wgl
ftl2ver | convert ftl to verilog testbench and vectors
ftrc | convert fsdb or wgl to FTL

## Slide 38
Confidential information
  The material is being disclosed to you pursuant to a non-disclosure agreement between you or your employer and Faraday. Information disclosed in this presentation may be used only as permitted under such an agreement.
Legal notice
  The information contained in this presentation is intended to provide a general guide as to which product is suited for a given requirement and shows suggested product applications. Specified functions and properties for products are only valid when handling instructions and other stated conditions and recommendations have been considered and followed. All descriptions, illustrations and dimensions in the information represent general particulars and do not form part of any contract. All information is provided “as is”, with no guarantee of completeness, accuracy, timeliness or of the results obtained from the use of the information, and without warranty of any kind, express or implied, including but not limited to warranties of performance. All information is subject to change without prior notice. Faraday assumes no responsibility whatsoever for any errors or inaccuracies about the information.